## Slide 1: Ozone and NO2 OSSEs on a Regional/Urban Scale for GEO-CAPE
Geo-cape OPEN COMMUNITY WORKSHOP
SEPTEMBER 1 2015
Vijay Natraj1, Brad Pierce2, Susan Kulawik3, Helen Worden4, Xiong Liu5, Mike Newchurch6, Konstantin Vinnikov7
1- Jet Propulsion Laboratory, California Institute of Technology, 4800 Oak Grove Drive, Pasadena, CA 91109
2- NOAA/NESDIS Center for Satellite Applications and Research, 1225 West Dayton Street, Madison, WI 53706
3- Bay Area Environmental Research Institute, Moffett Field, CA 94035
4- National Center for Atmospheric Research, 3450 Mitchell Lane, Boulder, CO 80301
5- Harvard-Smithsonian Center for Astrophysics, 60 Garden Street, Cambridge, MA 02138
6- University of Alabama and Huntsville, 320 Sparkman Drive, Huntsville, AL 35805
7- University of Maryland, College Park, MD 20742

## Slide 2: Goals
Utilize independent modeling systems for generation of Nature atmosphere and conducting assimilation impact experiments
Account for realistic atmospheric variability, which requires evaluation of the nature runs with respect to observations
  Include realistic variability in the synthetic radiances, which requires using realistic albedos and emissivities
  Include realistic sensitivities, which requires generation of averaging kernels (AK) for each retrieval for use in assimilation studies
Notes: These are the group’s goals, as they were in September.

## Slide 3: OSSE Flow Chart
Notes: There are three major components of the OSSE framework: Nature run (teal), Radiative Transfer/Retrieval System (purple), and Analysis System (orange).
We first used a set of representative profiles from 17 sites (hourly, every 3rd day of July 2011) and full radiative transfer/Optimal Estimation Retrievals (UV, UV-VIS, UV-VIS-TIR) to generate input data for developing a multiple regression estimate of the averaging kernels (AK).
We then use the AK regressions, the full Nature atmosphere (CONUS, hourly, every day of July 2011) to generate the Regional Multiple Regression AK retrievals (UV, UV-VIS, UV-VIS-TIR)
We then used observed GOES East and West Sounder cloud masks to identify clear retrievals, these are fed into the WRF-Chem/GSI regional assimilation system

## Slide 4: Quantifying Accuracy and Representativeness of Regional Nature Run
Correlation between model and ozonesondes at Beltsville and Edgewood
Correlation between model and EPA-monitored surface ozone (July 2011)
July 2011 Regional Nature run captures the variability of upper troposphere/lower stratosphere (200-100 mb) and boundary layer (1000-900 mb) ozone well but underestimates free tropospheric (400-300 mb) variance
Courtesy: M. Newchurch/L. Wang
Notes: The CMAQ component of the nature run provides the ozone below 300mb and used lateral boundary conditions from GFS, which doesn't have tropospheric chemistry and therefore doesn't provide realistic variability in the free troposphere. The nature run is a linear blend of CMAQ and GFS above 300mb and GFS captures the dynamically driven variability in the UT/LS.
The surface o3 is low at Trinidad Head because this is a coastal site that is mostly influenced by clean maritime air near the surface.

## Slide 5: Multispectral O3 Retrievals
Diurnally resolved Degrees of Freedom for Signal (DOFS) for different pressure ranges and spectral combinations for all GEOCAPE Regional OSSE sites (no VIS, UV, or UV/VIS retrievals between 02-09Z)
Note UV/VIS has the same spectral range and noise as TEMPO.
(nighttime)
Total Troposphere 0-2 km 0-1 km
VIS
UV-VIS
UV
UV-VIS-TIR
UV-TIR
TIR
VIS
UV-VIS
UV
UV-VIS-TIR
UV-TIR
TIR
VIS
UV-VIS
UV
UV-VIS-TIR
UV-TIR
TIR
VIS
UV-VIS
UV
UV-VIS-TIR
UV-TIR
TIR
Full Optimal Estimation Retrievals (UV, UV-VIS, UV-VIS-TIR)

## Slide 6: Nature/Retrieval Correlations
Regional Multiple Regression AK Retrievals (UV, UV-VIS, UV-VIS-TIR)
Diurnally resolved correlations between the Regional Nature Run and GEOCAPE O3 retrievals for July 2011 show:
UV-VIS-TIR shows the highest correlations in the mid and lower troposphere
UV-VIS shows improvement over the UV only retrievals below 800mb
More details in H. Worden’s poster
Notes: These statistics are based on direct comparisons between the Nature profiles (truth) and retrievals for all of CONUS for all of July 2011 and show the systematic improvement in retrieval sensitivity below 800mb as you go from UV to UV-VIS to UV-VIS-TIR. This is consistent with previous studies based on limited stations and provide a “real-world” context for how much information the retrievals have in the lower troposphere.
The reduced correlation at ~ 40mb is because of the low variability in ozone at these altitudes.

## Slide 7: Data Assimilation I
Initial RAQMS/WRF-CHEM/GSI GEOCAPE UV-VIS-TIR retrieval assimilation experiments have been conducted for early July, 2011
  Currently assuming 30% observational errors and only assimilating retrievals below 100mb due to large initial adjustments in the lower stratosphere
  Statistical analysis show positive impacts on surface ozone sampled at US EPA AIRNow sites
WRF-Chem Analysis
(O3, P)
Notes: The large initial adjustments in the lower stratosphere come about because we are simply adding the RAQMS ozone profile to the top of the WRF-Chem model top (50mb) to construct the full atmosphere profile before applying the AK. WRF-CHEM has coarse vertical resolution at the top and cannot resolve the sharp gradients in ozone in the UT/LS. The Nature run is influenced by GFS at these altitudes and so there are large differences.
We initially assumed 10% observational errors and assimilated the entire GEOCAPE profile. This resulted in propagation of the stratospheric adjustments into the lower troposphere (because of the AK coupling these layers in the analysis). We next tested a 30% observational error and the lower troposphere adjustments were reduced but not eliminated. Our final experiment only assimilated GEOCAPE profiles below 100mb, which largely eliminated the propagation into the lower troposphere although there were still large adjustments in the stratosphere due to the large vertical length scales in the background error estimates at these altitudes.

## Slide 8: Data Assimilation II
Future plans
  Improve observation error estimate using error estimates from Full Optimal Estimation retrieval for select stations
  Assess impact of restricting assimilation of retrievals to below local tropopause to mitigate impact of poor vertical resolution in WRF-Chem in the lower stratosphere
  Conduct regional UV and UV-VIS O3 assimilation studies
WRF-Chem Analysis
(O3, P)
Notes: WRF-Chem has poor vertical resolution in the lower strat because no one in the regional AQ modeling community cares about the UT/LS. We've been dealing with this issue for a number of years and I thought that since WRF-Chem is online the resolution would be OK given the need to predict u, v, T, and wv. We may have to increase the vertical resolution and raise the model top to improve the assimilation results. We'll have to explore this with some sensitivity experiments.

## Slide 9: Impact of Assimilation: Overall Results

## Slide 10: Impact of Assimilation: Selected Sites
Notes: Examples of nature vs control and UV-VIS-TIR assimilation for selected sites (upper left: Bakersfield CA, upper right: Chicago, IL, lower left: Gulfport, MS, lower right Legget, NC) showing realistic complexity in OSSE system (independent Nature/Analysis models; systematic improvements for clear sky stations (Bakersfield, CA), episodic improvements for cloud impacted stations (Chicago, Legget), and very small changes for stations with good agreement between control and nature runs (Gulfport, MS)

## Slide 11: NO2 OSSE Developments I
Spectral region: 400−490 nm (TEMPO spectral range)
Forward modeling approaches
  LIDORT
  Exact single scattering + two-stream multiple scattering (2S-ESS)
  2S-ESS + cross sections convolved to TEMPO spectral resolution (2S-ESS convolved)
Notes: Our previous runs (which were over a wider wavelength region) required 8hrs per day (15hrs of daylight) per station for the O3 UV-VIS using 44 cpus. For NO2, which has significantly larger spatial variability than O3, AK regression is unlikely to produce good results. Therefore, computational efficiency is critical.

## Slide 12: NO2 OSSE Developments II
Computational time (one scenario):
  LIDORT: 219 minutes
  2S-ESS: 295 seconds
  2S-ESS convolved: 78.5 seconds
Computational time (one day, full domain):
  LIDORT: > 8 years!
  2S-ESS: ~ 70 days
  2S-ESS convolved: 18 days
  With a 10x speed-up, we can perform calculations for one month for the entire domain in ~ two months

## Slide 13: Quantifying Accuracy and Representativeness of Regional Nature Run
PINNACLE, NY. Park Forest
BIRMINGHAM, AL. Urban
CENTERVILLE, AL. Rural
ATLANTA, GA. Urban
YORKVILLE, GA. Rural
PENSACOLA (OLF), FL. Urban
GULFPORT, MS. Urban
Observed & Modeled (Nature run) diurnal cycle of NO2
STATIONS MAP
The model systematically overestimates NO2 concentrations but correctly reproduces shape of diurnal cycle and differences of NO2 concentrations between rural and urban locations.
Modeled and observed daily variability in diurnal cycle of NO2 concentrations are quite consistent.
Courtesy: K. Vinnikov/R. Dickerson/N. Krotkov

## Slide 14: NO2 Retrievals: First Results
Preliminary retrievals with TEMPO instrument characteristics meets GEOCAPE requirements for column precision
We retrieve a profile and collapse into a column
NO2 has sensitivity in the lower troposphere and stratosphere
There is limited profile information for NO2
Work underway on increasing computational efficiency to meet processing demands for full domain

## Slide 15: Conclusions
O3 Regional OSSE experiment underway
Work ongoing on tuning the analysis system
Initial results promising
Full UV-VIS-TIR retrievals showing positive impact on surface O3
Regional OSSE system showing realistic complexity
NO2 forward modeling simulations underway

## Slide 16: Backup Slides

## Slide 17: Nature Run
4 km
down
scaling
1.33 km
Urban Nature Run
12 km
Regional Nature Run
Courtesy: K. Pickering/C. Loughner
Notes: These are the outputs – drop this

## Slide 18: AK Prediction
Multiple regression works best for surface – 681 hPa
Combinations of fit AK in lower troposphere and average AK above allow simulated observations for different wavelength combinations
UV-VIS-TIR provides highest correlation between simulated observations and nature run
See Helen’s poster for more details
Notes: Replace this with regional multiple regression retrievals slide from today. Dofs are reflected in actual correlation

## Slide 19: Retrieval Biases
Diurnally resolved biases between the Regional Nature Run and GEOCAPE O3 retrievals for July 2011 show generally low biases (<20%) except:
between 200-300mb at sunrise and sunset (UV and UV-VIS only)
at the surface (underestimate daytime and overestimate nighttime O3
Regional Multiple Regression AK Retrievals (UV, UV-VIS, UV-VIS-TIR)
Notes: These statistics are based on direct comparisons between the Nature profiles (truth) and retrievals for all of CONUS for all of July 2011 and show the systematic improvement in retrieval sensitivity below 800mb as you go from UV to UV-VIS to UV-VIS-TIR. This is consistent with previous studies based on limited stations and provide a “real-world” context for how much information the retrievals have in the lower troposphere.

## Slide 20: Impact of Assimilation: Overall Results
Nature vs Control (Eastern US)
Nature vs Assimilation (Eastern US)
Nature vs Control (Western US)
Nature vs Assimilation (Western US)
Notes: Systematic reduction in surface ozone bias between nature run (obs) and UV-VIS-TIR analysis (mod) compared to control (mod) at US EPA AIRNow sites for July 1-5, 2011

## Slide 21: Accomplishments for Ozone OSSE
12 km and 1 km Nature simulations were evaluated with respect to observations during the 2011 NASA DISCOVER-AQ campaign.
Diurnally resolved high spectral resolution UV/VIS/TIR forward modeling at 14 representative sites using ozone, NO2, HCHO, SO2, aerosol, water vapor, and temperature profiles from the Regional Nature run has been completed.
TIR, UV, VIS, UV/TIR, UV/VIS, and UV/VIS/TIR ozone retrievals have been generated and evaluated with respect to the Nature run profiles.
Notes: Don’t need this slide

## Slide 22: Accomplishments for Ozone OSSE
Averaging Kernel (AK) regression based on instrument and observing parameters has been developed using retrievals from 14 representative sites.
Data assimilation shows positive impacts on surface ozone sampled at US EPA AIRNow sites.
Notes: Don’t need this slide

## Slide 23: NO2 OSSE Developments
Ways to get 10x speedup
  Optimize optical property initialization (mainly, aerosol phase function moments)
  Remove redundant copying of data between variables
  Separate operations that are the same for each profile (e.g. reading in of large aerosol optical property tables) from those that are different between profiles so that former needs to be done only once

## Slide 24: NO2 Retrievals: First Results
Preliminary retrievals with TEMPO instrument characteristics meets GEOCAPE requirements for column precision (OBServation error includes precision and error from aerosols, albedo)
Work underway on increasing computational efficiency to meet processing demands for full domain
NO2 has sensitivity in the lower troposphere and stratosphere
We retrieve a profile and collapse into a column
There is limited profile information for NO2