## Slide 1: Spatially resolving ocean color and sediment dispersion in river plumes, coastal systems, and continental shelf waters.
Dirk Aurina,b,, Antonio Manninoa, & Bryan Franza
aNASA Goddard Space Flight Center,
b Science Systems and Applications, Inc.
Funded by the GEO-CAPE mission pre-formulation activity. Acknowledgements to M. Ondrusek of NOAA/NESDIS, X. Xiong and A. Angal of NASA/MCST, and G. Meister of the NASA/OBPG.

## Slide 2: Stepping Out
705 km
LEO
36,000 km
GEO

## Slide 3: Possibility & Opportunity

## Slide 4
What resolution is needed? Where do we need it? Why?

## Slide 5: Specifically:
Ground Space Distance (GSD): Spatial resolution requirements in dynamic coastal and nearshore environments
GSD in quiescent waters (i.e. more relaxed spatial res. reqs reduce “stare interval” for telescope  higher temporal res.)

## Slide 6: Specifically:
Scales of Variability (“patchiness”) near-, offshore
Proportion of Variability resolved at given GSD

## Slide 7: Approach
5 Regions of Study: 4 Plumes, 1 subtropical gyre
Wet Season & Dry 2008-2011 (3,000+ images)

## Slide 9: NIR-SWIR Merge
(See Poster: Murky Waters; Atmospheric Correction and MODIS Ocean Color Uncertainty in Extreme Environments.)

## Slide 10: 2 Methods for Quantifying Spatial Scales of Variability
1. Optimal GSD by Virtual Transect
  Resolution requirements
2. Semivariance (γ)
  Spatial scales of patchiness
  Proportion of variability resolved at optimal GSD

## Slide 11: Method #1 Finding the optimal GSD: Interpixel variability around virtual stations
Finding the optimal resolution:
At each station, ask, “Is the interpixel variability greater than the noise?”
If “yes” then natural variability is detected, and using a larger pixel size will overlook variability at that scale.

## Slide 13: Calculating the Ocean Color Uncertainty
PACE Mission Science Definition Team Report
NASA MODIS Characterization Support Team (MCST)
Evaluated on each pixel depending on whether SWIR or NIR bands used for atmospheric correction (more later)
SNR
AC
(See Poster: Murky Waters; Atmospheric Correction and MODIS Ocean Color Uncertainty in Extreme Environments.)

## Slide 14: Method #2 Finding scales of variability: Semivariograms
The semivariance function = half the squared difference of all pixel pairs in an image at distance h from each other in any direction, over all distances. The data can generally be fit to a spherical model:

## Slide 15: Results

## Slide 16: Example: Hurricane Irene and TS Lee;
Aug 27 – Sept 7, 2011 (Aqua 9/11/11 shown here)
Cloud ID
failure

## Slide 18
Chesapeake: 630 Mississippi: 803 images
Results; Optimal GSD

## Slide 19: Results; Optimal GSD

## Slide 20: Results; Semivariance

## Slide 21: Summary
Several years of high resolution (250 m) ocean color imagery from the most turbid and dynamic environments were custom-processed and analyzed for spatial variability.
Pixel-specific estimation of ocean color uncertainty is possible and useful.
Plumes more heterogeneous than nearshore, shelf, or offshore
  Optimal GSD ↑ from ~500 m in plumes to ~1,400 m offshore
  Patches ~20-90 km vs 180 km offshore
  Plume patch size ↑ with river size
> 90% of variability generally resolved at 500 m GSD
Aurin, Dirk A., Mannino, A., Franz, B., "Spatially resolving ocean color and sediment dispersion in river plumes, coastal systems, and continental shelf waters. Remote Sensing of Environment." RSE-D-13-00194, in review.

## Slide 23: extras

## Slide 24
Sargasso: 1,100 images
Results; Optimal GSD

## Slide 25: Results; Optimal GSD
Mississippi: 803 images Yangtze: 757

## Slide 26: Results; Semivariance

## Slide 27: Results; Semivariance