## Slide 1
Michael J. Newchurch1*, Shi Kuang1, Lihua Wang1, Thierry Leblanc2, Raul J. Alvarez II3, Andrew O. Langford3, Christoph J. Senff3,4, Steve Brown3, Bryan Johnson3, John F. Burris5, Thomas J. McGee5, John T. Sullivan5,6, Russell J. DeYoung7, Johnathan Hair7, Jassim Al-Saadi7, Gao Chen7, Matthew Johnson8, Barry Lefer9, Brad Pierce10, Edwin Eloranta10
TOLNet – A Tropospheric Ozone Lidar Profiling Network for Satellite Validation and Process Studies
http://nsstc.uah.edu/atmchem mike@nsstc.uah.edu Aug. 30-Sep. 2, 2015, Research Triangle Park, NC
1UAH, 2Caltech/JPL, 3NOAA/ESRL, 4CU, 5NASA/GSFC, 6ORAU, 7NASA/LaRC , 8NASA/ARC, 9NASA/HD, 10UW
Introduction
NASA initiated an interagency ozone lidar observation network under the name TOLNet to promote cooperative multiple-station ozone-lidar observations to provide highly time-resolved (few minutes) tropospheric-ozone vertical profiles useful for air-quality studies, model evaluation, and satellite validation.
Motivation:
Prepare to make best use of next-generation satellite tropospheric ozone observations by advancing the understanding of following processes:
Synoptic processes such as STE, long-range pollution transport, and large-scale stagnation [timescale: days to several hours].
Mesoscale processes such as diurnal land/water boundary cycles, low-level jets, and orographic venting [timescale: hours].
Local scale processes including exchange between the boundary layer and the free troposphere, episodic precursor emissions, and convection [timescale: sub-hourly].
Objectives:
Provide coordinated high-resolution measurements of tropospheric ozone for air-quality/chemical/transport model improvement and satellite retrieval validation.
Exploit synergies with EVS-1 DISCOVER-AQ, EVI-1 TEMPO, GEO-CAPE studies, and existing routine observations to advance understanding of processes controlling regional air quality and chemistry.
Develop recommendations for lowering the cost and improving the robustness of ozone lidar systems.
2015 GEO-CAPE Workshop
Stations
Name | JPL TMO (Table Mountain tropospheric Ozone) DIAL | TOPAZ (Tunable Optical Profiler for Aerosol and oZone) lidar | RO3QET (Rocket-city O3 Quality Evaluation in theTroposphere) lidar | GSFC TROPOZ (TROPospheric OZone) DIAL | LMOL (Langley Mobile Ozone Lidar)
Affiliation | NASA/JPL | NOAA/ESRL | UAH | NASA/GSFC | NASA/LaRC
Host location | Wrightwood, CA | Boulder, CO | Huntsville, AL | Greenbelt, MD | Hampton, VA
Set-up | Fixed-location | Mobile | Fixed-location | Mobile | Mobile
Transmitter type | Quadruple Nd:YAG pumped Raman laser | Quadruple Nd:YLF pumped Ce:LiCAF laser (tunable wavelength) | Quadruple Nd:YAG pumped Raman laser | Quadruple Nd:YAG pumped Raman laser | Quadruple Nd:YLF pumped Ce:LiCAF laser (tunable wavelength)
Wavelength (nm) | 289, 299 | Typically 287, 291, 294 | 283, 289, 299 | 289, 299 | Typically 285, 291 (527 for aerosol)
Receiver size (cm) | 91, 5, 5 | 50 | 40, 10, 2.5 | 41, 2.5, 2.5 | 40
Measurable range (km AGL) | 0.1-23 | 0-3 | 0.1-12 | 0.2-12 (day) 0.2-19 (night) | 0.1-4
Table 1. Summary of the TOLNet lidars.
Measurements
310K (≈2 to 4 km ASL)
May 24, 2013 12UT RAQMS 310-K ozone
Brad Pierce (NOAA/NESDIS)
TMF
(Leblanc)
ESRL (Senff & Langford)
UAH
(Newchurch &
Kuang)
Figure 2. Multiple-station measurements of two stratospheric intrusions on May 24, 2013. (note the ESRL observation was made at Las Vegas.)
Due to smoke
Due to smoke
Ozonesonde
UAH O3 Lidar
UW-HSRL
LaRC DIAL & HSRL
Figure 3. Ozone enhancement associated with smoke transport measured by the ozone DIAL and HSRL on August 14, 2013.
Measurements
Figure 1. The effect of transport and mixing processes on the relationship between column and surface ozone observed with lidar during Discover-AQ/FRAPPE. In 66% of all cases observed at BAO, 1500 m AGL O3 column and surface values agree within 10 ppbv, almost exclusively occurred after midday LT. For the remaining observations (34%), column O3 mostly exceeds the surface values.
Senff et al.
Mean and 1-sigma
Mean and 1-sigma
Mean and 1-sigma
Figure4. TOLNet lidar intercomparison during DISCOVER-AQ campaign at BAO in July 2014.
Data Accuracy Assessment
Summary and Conclusions
A main objective of TOLNet is to provide high-resolution lidar data at multiple stations to modeling and satellite teams for validating and improving the fidelity of tropospheric ozone measurements by NASA’s next-generation geostationary instruments.
TOLNet lidars agree with ozonesonde free flights and tether flights, with CRDS on the BAO carriage, and with each other to within ~ 10% over a wide variety of conditions.
The TOLNet data are accessible at
http://www-air.larc.nasa.gov/missions/TOLNet/.
NOAA/ESRL TOPAZ sample size = 30967
mean = 62.6 ppbv
std dev = 8.4 ppbv =13%
NASA/GSFC TROPOZ sample size = 158203
mean = 60.9 ppbv
std dev = 8.5 ppbv = 14%
Diff. of mean = 3%
Diff. of std dev = 1%