## Slide 1: GEO-CAPE Aerosol Working Group Report
9/2/2015, GEO-CAPE workshop
Quote: “Reports should say whether the White Paper captures your high-level accomplishments to date (and if not, say what is missing). Also please make your recommendations for future work, FY16 and possibly FY17”

## Slide 2: Aerosol WG high-level achievements (comments for the GC white paper)
Assessment of aerosol retrieval availability and accuracy as a function of instrument pixel resolution based on the MODIS analysis has led to a recommendation of instrument resolutions (2x2 km and 1x1 km for threshold and baseline mission, respectively) for GEO-CAPE aerosol objectives
With the selection of TEMPO (and the tech specification), the synergistic retrieval of TEMPO and GOES-R becomes necessary to meet the minimum GEO-CAPE aerosol objective. Information content analysis suggested a strong synergy between TEMPO and GOES-R for reducing the uncertainties in retrieving AOD and fine-mode AOD
A numerical testbed is constructed for providing objective assessment of aerosol information content for constellation of sensors and algorithms for observing capabilities including the characterization of aerosol plume height. Unified retrieval algorithms are being evaluated using the existing satellite data and capability
Capability of retrieving aerosol absorption and SSA for pollution and biomass burning aerosols from UV and blue wavelengths has been demonstrated with promising results
Values of the daytime varying measurements of AOD on calculating aerosol radiative forcing compared to the LEO AOD has been shown using the daytime variation of AOD from AERONET and LEO AOD from MODIS
Aerosol retrieval from aircraft remote sensing hyperspectral instrument of GeoTASO has been demonstrated for TEMPO applications.

## Slide 3: On-going work (into FY16)
GLI as a testbed of TEMPO/GOES-R synergy Evaluation of surface reflectance with CAR measurements and assess the Lambertion assumption of surface reflectance in the UV wavelength
Aerosol retrieval algorithm testing with the synthetic radiance from the GEOS-5 Nature Run (G5NR, 7-km resolution, clear sky only)
Retrieval of surface PM2.5 possibility and accuracy from the AOD retrieval from the G5NR
Continue development of a hyperspectral aerosol retrieval algorithm that can retrieve spectral AOD, surface reflectance, and other aerosol properties from GeoTASO.

## Slide 4: Other activities in FY16 and beyond
Quantify the aerosol effects (amount, height, optical property) on gas retrieval (NO2, SO2, ozone) and effects of NO2 and other gas on aerosol retrieval (collaboration between AeroWG and Vijay)
Using the MAIAC surface reflectance at 412 nm for trace gas (NO2 and ozone) retrieval (collaboration between AeroWG and PK/Nick?)
Explore the aerosol science opportunity with the GEO-CAPE ocean color measurements over coastal areas (diurnal variations of megacity air quality, aerosol-coastal meteorology interactions/feedbacks, intercontinental transport fluxes, pollution and fire emissions, aerosol type identification)
Involve in the KORUS-AQ field campaign (May-June 2016) for retrieval algorithm testing and validation and assess the value of GEO observation, taking advantage of the aerosol measurements in many dimensions (size, composition, vertical distribution of concentration, extinction, absorption, polarization, and GEO observations from GOCI)
Toward an unified hyperspectral aerosol retrieval algorithm that can retrieve AOD, aerosol size, aerosol type, aerosol absorption, and at least one piece information of aerosol profile by a combined use of hyperspectral measurements in both UV, VIS, NIR, and TIR