## Slide 1: Systematic Vertical Correlation of O3 and Optimal Estimation Provide Remarkably Accurate Methods for “Near-Surface” Ozone — Two Related Methodologies
Trinidad Head, CA
Pacific Coast
Yarmouth, NS
NE Atlantic Coast
Huntsville, AL
Interior Southeast
Beltsville, MD
Eastern US
Robert B Chatfield (NASA Ames), Xiong Liu (Harvard Smithsonian), Robert F Esswein (NASA Ames/BAER)
and the GEO-CAPE “Sensitivity” and “Variability” science definition teams
GEO-CAPE Workshop, 12 May 2011

## Slide 2: Outline
“Near-surface” ozone: ignore surface variations irrelevant to ozone load for the day
Layering of lower tropospheric ozone…discouraging
Layer average ozone -> Surface estimation encouraging
Optimal Estimation: Vert. Resolution well described; Accuracy needs detailed work
Grounds for optimism in characterizing near-surface ozone — what are “exceptional events”?
“Just the Physics” vs our expectations for best estimation of accuracy — region by region..

## Slide 3
1/28/2011
18-25 25-30 30-35 ppbv
UAHuntsville Campus Ozone
Measured with ozonesonde
Percent difference reaches ~30% for measurements away from buildings.
Inside
Horizontal Variability
June 19
Surface ozone of 24 sonde profiles compared with local EPA site: The variance in the surface ozone amounts at the ozonesonde/lidar site seen in the EPA HSV-Airport Rd. site (~10 km distant; Summer 2010) is about 75%. The other 25% is the HORIZONTAL variance.
Mike Newchurch
slide

## Slide 4: Different variation structures for ozone and aerosol suggest local photochemistry dominates the production
Ozone mixing ratio, August 4, 2010
Aerosol ext. coeff. at 291nm from O3 DIAL
O3 diurnal variation
The rapid aerosol variation in the PBL suggests the importance of a collocated aerosol measurement.
Mike Newchurch
slide
Notes: Kuang: This slide is to demonstrate the aerosol is not necessarily correlated with ozone depending on their sources. I suggest using the previous one, slide 3, to emphasize lidar’s significance for satellite and skip this one.
Use either the previous slide or this one but not both? Needs a “so what” message. With a DIAL you’ll get the aerosol anyway, right?

## Slide 5
Beltsville, MD
Eastern US
Beltsville, MD
Eastern US
Analyses of variability from layer to layer of ozone … no averaging Black lines indicate variability near surface

## Slide 6: Satellites sense layer averages, and this aids surface O3 estimation immensely
Red lines show correlation of layer average ozone with “near-surface” ozone (Sfc-950 hPa).
Thermal IR retrieval - green
UV+IR retrieval – red
UV+Vis nearly as good

## Slide 8: SE USA: Low-Cloud exchange of pollution
Important effects persist for days, from one cloud system to another
Thickens the high-ozone layer
Raises ozone to a region more visible to the OMI sensor
  depends on back scattered radiation

## Slide 9: We may estimate various layer depths
East-Coast
West (NW) — ozone above lowest layers
Influenced by Asian, STE lamina

## Slide 10: IR and UV Averaging Kernels
Mike Newchurch
slide

## Slide 11: Current Natraj et al (2011) estimates of vertical resolution depend mostly on radiation/retrieval technique, not test profiles
Since we are primarily interested in near-surface ozone, we sum the Degrees of Freedom for Signal up, layer by layer, from the lowest layer.
Note the opposite virtues of UV+Vis (great in lowermost troposphere, then no more info)
and TIR (near-0 sensitivity to 925 hPa, but increasingly good up to 500 hPa.
UV+Vis
TIR
UV+TIR
UV+Vis+TIR

## Slide 12: Current results suggest amazing accuracy for estimation of layers

## Slide 13: Strong vertical Autocorrelation in Natraj test profiles Wide selection of possible profiles allows regional variation of tropospheric ozone to affect calculations! Correlation significantly greater than sonde-stations results
1:1
regression

## Slide 14: Alternative Methods For Appropriate Accuracy Estimates
“Standard” Rodgers-style: Radiation and retrieval improve best estimate including geophysical correlation.
For every region and season of interest, perform sensitivity studies of radiative transfer / retrieval as in Natraj,
but use an adequate sample of ozone soundings. Existing knowledge initiates the retrieval “close to Nature.”
Sounding sets characteristic of the region provide the important “a priori covariance” matrix, give an appropriate first guess, and influence the solution. Remarkably good correlation of test profile and retrieval can occur.
Run as many different regional examples as possible, e.g., ~5–10 “regions.”
B. “Just the physics” solution: Bayesian estimation (improvement-of-our-knowledge philosophy) using an “uninformative prior.” Use “sample profiles” chosen to give minimal prior information. Test profiles can exhibit little vertical correlation, by design, and a priori and first-guess solutions are as uninformative as possible, but allow convergence. The solutions maximize information from the radiation pattern itself.
Secondly, add information about vertical autocorrelation (layer-average to surface regressions) and similar information.
This technique can use added information from any region in the continent.
Appealing to many, but formulation is intricate, some formulations may not even converge. (Hence the popularity of the Rodgers method.)

## Slide 15: “Just-Physics” then statistics: B

## Slide 16: Traditional Technique: A

## Slide 17: Nocturnal ozone enhancement associated with low-level jet
Aerosol ext.coeff. at 291nm from O3 lidar
Co-located ceilometer backscatter
(a)
Low-level jet
Co-located wind profiler
Positive correlation of ozone and aerosol due to transport
Oct. 4, 2008
Kuang et al. submitted to Atmospheric Environment
Aerosol
Lidar
Mike Newchurch
slide
Notes: Kuang: Ozone and aerosol plums rise the same time as the LLJ. But the time range of the lidar data acquisition did not fully cover the LLJ. So added a dashed circle to label the LLJ.
What is the take home message here? According to your circles, most of the ozone action seems well in advance of the jet, 1-2 UTC. Aerosol really kicks up later, 3-5 UTC

## Slide 18
Sun
Satellite
scattering N2,O2
Situations with scattering aerosol gives more info on near-surface ozone: Rayleigh scattering of Chappuis, longer-wavelength light is amplified by aerosol scattering
Earth’s surface
Aerosol effects can aid or hinder retrieval
Rayleigh n
For a given incident frequency n
Higher altitude or absorbing aerosol degrade abilities

## Slide 19: FIN
Good reason for great optimism about that we can characterize regional near-surface ozone