## Slide 1
Effect of NO2 on Geostationary Satellite Chlorophyll Retrieval In Coastal Water:
False Diurnal Variation
Jay Herman & Maria Tzortziou
Annual Average NO2 Climatology from OMI

## Slide 2
OMI
Examples of NO2 Diurnal Variation
OMI observed pixel NO2 variability for Sept. 30, 2005 over eastern and central US with clouds. Areas covered with clouds have no current NO2 information.

## Slide 4
Input to Radiative Transfer Equation
Measured Reflectivity of Chesapeake Bay
[Tzortziou et al., 2007]
Including Chlorophyll and CDOM

## Slide 5
The Effect of NO2 Altitude Distribution
Use 0 - 3 km Case
In following slides
0–2 km
0–4 km
0–3 km

## Slide 6
Output from Radiative Transfer Equation
Reflectivity Change per DU of NO2
dR/R = -0.01*(3.84243 + 0.08821*exp(SzaEff/14.91337)) Wvl=490 nm
dR/R = -0.01*(7.42119 + 0.40409*dexp(SzaEff/18.29943)) Wvl=443 nm
490 nm
443 nm

## Slide 7
Chlorophyll Blue/Green Ratio From MODIS Website
data a0,a1,a2,a3,a4/ 0.3660,-3.0670, 1.9300, 0.6490,-1.5320/
x = log10( ratio(i))
x2 = x*x; x3 = x2*x; x4 = x3*x
Ca(i) = 10**( a0 + a1*x + a2*x2 + a3*x3 + a4*x4 )
Retrieval Error per DU of NO2
P = Ca = A R –N
dP/P = -N dR/R * [NO2]
The Power Coefficient N is the key to the magnitude of the NO2 false diurnal variation effect on retrieved chlorophyll values

## Slide 8
Case 1
Case 3
Case 2
Measured NO2 Amounts vs Time of Day

## Slide 9
Case 1: An Example of False Diurnal Variation in Chlorophyll

## Slide 10
Case 2: An Example of False Diurnal Variation in Chlorophyll

## Slide 11
Case 3: An Example of False Diurnal Variation in Chlorophyll

## Slide 12
Case 1,2,3: An Example of False Diurnal Variation in Acdom
Since Acdom, depends R490,
the percent error per DU of NO2
is reduced compared to retrievals
based on R443

## Slide 13
Summary
NO2 can be highly variable throughout the day.
Using an incorrect assumed value of NO2 affects the retrieved water leaving radiance nLw and can be interpreted incorrectly as chlorophyll absorption.
Chlorophyll retrievals errors can be over 50% based on using an assumed NO2 amount from another instrument or climatology.
NO2 should be measured at the same time that coastal ocean water leaving radiances are measured.