## Slide 1: Lessons learned from OMI observations of point source SO2 pollution and suggestions for GEO-CAPE requirements
N. Krotkov (NASA/GSFC)
V. Fioletov, C. McLinden (Environment Canada)
K. Yang (Univ. of Maryland)

## Slide 2: Lesson 1: Averaging OMI pixels allows detection of weak sources with enhanced ground resolution
SO2 signal may be not detectable in a single OMI pixel. This rectangular “pixel” is light pink
However, it is possible to see the source and even to determine its exact location by averaging a large number of individual satellite pixels.
In this plot, a pixel is light pink if it covers the source (x) and it is white otherwise.
x

## Slide 3: We used SO2 Emissions source inventory (for 2006) (thanks to Mike Moran et al., Environment Canada)
Top 100 emission sources for the US
Top 20 Canadian emission sources
Sources located within several km were combined into one
The largest “combined” source is about 300 kT per year
The largest single US source is about 200 kT per year
The oil sands site emissions are about 120 kT per year

## Slide 4: We used OMI PBL SO2 data to examine average spatial patterns from the top pollution point sources
OMI daily SO2 data do not show any obvious pollution signals except for exceptionally strong sources (e.g., Norilsk, Russia and Ilo, Peru smelters, China)
We applied:
Data filtering:
  by Cross-track position (10-50)
  by cloud fraction (<0.2)
  by solar zenith angle (<60)
  by SO2 values (to remove outliers and volcanic SO2)
Spatial smoothing
Local bias correction
No AirMass Factor adjustment [ Lee et al 2009] - this will be implemented in Level 3 SO2 data due to release in May

## Slide 5: Mean total column SO2 and NO2 values for 2 sites (Mildred Lake and Fort Chipwyan) as a function of the distance between the site and the pixel centre
-- Fort Chipwyan
-- Mildred Lake
The whiskers show the 5th and 95th percentiles, the box edges represent the 25th and 75th percentiles, the center is drawn at the median value.
We found that point sources of SO2 in the US produce elevated SO2 values over a relatively small area: within 20km

## Slide 6
60 km
60 km
SO2 from OMI, average for 2005-2010
For each grid point of a 2x2 km grid, all overpasses centered within a 12 km from that point were averaged
OMI smallest
pixel size

## Slide 7
SO2 Source #10 (John Amos power plant, 2900 MW, ~110 kT/year of SO2)

## Slide 8
US Source #1.Bowen Coal Power Plant, Georgia (3500 MW),
SO2 emissions: 170 kT in 2006
“In 2008, the mammoth construction program yielded the first scrubbers, sophisticated equipment that will reduce our overall systems emissions by as much as 90 percent”
Georgia Power website
2005-2007
2008-2010

## Slide 9: OMI data show a substantial decline in mean SO2 values over Western US between 2005-2007 and 2008-2010
2005-2007
2008-2010

## Slide 10
Mildred Lake, Alberta, Canada. Oil Sands.
Mean OMI SO2 for May-August
2005-2007
2008-2010
Lesson 2: Important SO2 targets outside CONUS

## Slide 12: Annual SO2 emissions vs. and estimates from a fit of mean OMI SO2 by 2D Gaussian function (2005-2007 data)
Fit
where
If is in DU, i.e. in 2.69·1026 mol·km-2 , and σx,σy are in km, then a is in 2.69·1026 mol.
Since , a is the total number of molecules.
Mean OMI SO2 Fit Residuals
Y = 0.0056 X
R=0.78
for sources<150kT/year
R=0.88 for all sources
Lesson 3: It appears that OMI SO2 data can be used to monitor sources that emit more than 80 kT per year

## Slide 13: Suggestions for GEO-CAPE measurement requirements:
High spatial resolution (a few km) is required for emission monitoring.
Increase SO2 measurement precision requirement: ~0.1 DU ~ 1015 molecules / cm2
Plan for frequent measurements of selected regions: (~100/day )
Staring mode of observations including targets in Canada
(e.g., Oil Sands), Mexico and S. America (Peruvian smelters, degassing volcanoes )